## Slide 1
Amazon car State PoC
Feb 26, 2025
Renesas AI - COE
Renesas Electronics Corporation

## Slide 2: Summary
As part of a quick proof of concept, Renesas's AI-COE team implemented an AI model to determine the state of the car. We focused on three conditions:
Car-On (with air-conditioning)
Car-Off.
Driving.
We collected ~8 minutes of data using a single axis accelerometer mounted on interior of the car. Resulting model gave 99% K-Fold accuracy. This indicated that the problem is solvable if appropriate data is collected for a production deployment.
Using e2-studio AI plugins & Reality AI Tools, we were able to develop a quick prototype in < 1 hours --> demonstrating the ease-of-use for our toolset.

## Slide 3: Setup - Driving Car
Single axis accelerometer attached to car using tape.
AIK-RA6M3 (ARM Cortex M4) used for data collection and inference/ model deployment.
Collect data for CAR ON (with ac), CAR OFF and DRIVING categories.
Used Toyota Prius for this PoC.
Collected ~8 minutes of data for quick prototyping.
Data Collection Setup

## Slide 4: Data collection using Data Storage Tool
Reality AI - Data Storage Tool in e2-studio IDE
Renesas AI Plugins provide easy to use interface to collect data, test & validate models.
As part of the setup, we used these plugins via e2-studio IDE to collect data & test the models.

## Slide 5: Data segmentation
Reality AI Tools preprocesses the data by breaking it down into smaller blocks. We call these blocks – segments.
These segments are then used to train and test the model. Purpose of this preprocessing step is to make sure model is trained on data it's going to see live – i.e small blocks or segments.
Reality AI Tools – Curate Page for Segmentation of the Dataset

## Slide 6: Results - Model Training
Achieved 99% K-Fold accuracy on the collected data.
Best performing model used Spectral Shape feature space
Feature Space used: Spectral Shape
Flash = 11.6 KB
RAM = 3 KB
Multiplication Operations: 10752
      Feature Space: 4608
      Classifier: 6144
Model: Support Vector Machine (One VS One decision structure).
K-Fold Accuracy Confusion Matrix

## Slide 7: Feature Explanation – Spectral shape
This is a decision significance plot showing relative importance of the frequency bands; the more orange, the more significant to the decision.
Interpretation: This shows that low frequency range is more significant in making the distinction between car-off and car-on. The signals have significant peaks at frequency below 100 Hz. This suggests that a much lower frequency range can be used to re-train a smaller classifier using lesser resources
How its calculated: First we compute the absolute value of the real portion of the FFT. This is also referred as an amplitude spectrum in signal processing. It represents power transmitted by each frequency in the spectrum.
Computed value is then normalized. Because of the normalization, the spectral shape feature space is not sensitive to increased wave amplitude or power.
Feature Space Decision Significance Plot

## Slide 8: MCU/ MPU Selection
Reality AI Tools MCU/ MPU Selection module can assist in figuring out the right MCU needed to deploy the model.
The module directly links to the Renesas Part Selector with various MCU/ MPU options to select from.
Note: The model selected for testing was just one of the option available for live testing. This does not indicate any final solution. We have a range of models available for testing. Some of them require Flash memory as low as 600 bytes and a RAM of 62 bytes only. These models can fit any RA, RX, RL78 & RZ cores available across Renesas portfolio.
Tools MCU/ MPU Selection Module
Renesas Part Selector